Digital Multimeter
Cameron McGary, Joel Castro

---
Why this project?
- Experiment with output via LCD
- Utilize the A/D conversion in the AVR
- Try to create a usable device without being tied to a PC's serial/USB port

---
Components of this project
- Amplifiers
- Power Supply
- LCD Screen
- The ATMEGA88PA chip

---
ADC Amplifiers
- The ADC is limited to measuring ~1.1V or less.
- In order to create a usable device, the probes must be able to measure more than this.

---
MDL-16166-LS
- Difficult initialization
- Limited number of pins on AVR
   - Sharing pins temporarily
- 14 pin LCD
- 4/8bit setup
- 16:1 mux Display

---
AVR
- 28 Pins (enough)
- 6+ ADC
- C Programmable
  - AVR tool chain
- Low power
- Fast conversion
- “Well known”

---
Power Supply

---
LCD Initialization
- Difficult but straight- forward
- Follow the steps!
- Check you options.
- Don't Forget Time Delays!
- Don't connect to USART!

---
LCD Options
←most important part
←pretty useful
↓ for more complexity

---
More Information on LCD
- Get the Varitronix LCD Initialization Instructions
- Alternative instructions:
  - http://courses.eece.maine.edu/ece177/
  - 16166 is a standard Hitatchi HD44780 LCD
  - Other LCD's use same instructions
    - Change mux setup
    - LED backlight

---
Start Multimeter
Initialization