 FIR Filter Design

The code for the FIR filter is rather straightforward. The first thing that was done was a plotting of what the passband and stopband was to be on the graph. This was just a graphical presentation of what was desired so that it would be easier to tell if the specifications had been met. The next part was to record the number of samples and the order of the filter to be used in the function to actually create the filter. By simply changing the stored value of the filter order, modifying the filter t meet specs would be much easier. It is also necessary to normalize all frequencies which was done by simply creating a array that went from 0 to N-1 and dividing all of these by the number of samples N. This would give a frequency range of 0 to 1. Another important step is to make sure filter is linear phase. In order to make sure it is linear phase, the filter must have symmetry around around the center of the samples. The operation to make it symmetric was to simply duplicate the left half of the frequency range on the right side in reverse. Since the function is symmetric around the origin or at the first sample 0, the left side can be replaced by the N/2 sample that are immediately left of the origin. This is expressed in the following excerpt from the code : f(N/2+1+1:end) = f(N/2+1+1:end)-1;.

Now that the filter specifications and frequencies have been set up, the desired filter can be defined according to those specifications. To do this, the equation for the desired filter looks like this:
Hd = (abs(f) < wp) .* 10.^(Ap/20). Here, the wp refers to the passband frequency for a simple lowpass filter. The Ap refers to the maximum gain that can be attained at the passband frequencies. The attenuation of the stopband can be determined by the filter order as well as the values chosen for wp and Ap. The desired filter in this case was a low pass filter so a filter defined as Hd = (abs(f) < .1) .* 10.^(.1/20) would be satisfactory for a start. Setting the filter order to a relatively high filter order and then lowering it down gave a function closer to the edge of the specifications. To also help lower the filter order, which is a primary goal of filter design, the values of Ap and wp were changed but kept close to the original. Lower both these values gave the filter more room – that is improved the gain and attenuation – so that the order of the filter could be decreased more as well.

Once the filter was designed, it was made casual by shifting it right. This was accomplished in the code by multiplying the function be e-j2πf*(M-1)/2, where M is the filter order. It was also critical to decide the typ of filrter to be used oin the design process. After taking the inverse fast fourier transform, the desired filter we designed needs to be used by a Matlab filter generating function such as kaiser() or butter(). These will create different kinds of filters that have different properties that may require lower filter orders or be more equiripple. For the FIR filter, the Kaiser filter was initially used and lowered to the lowest filter order using the method discussed previousy. We set the Beta value to 8 which provided a sidelobe attenuation of 80dB based on the equation for the value found in the help files. The equation is shown below where β is the value to be input into the function and α is the attenuation desired.

 The Chebychev (Чебышёв) filter turned out to be more efficient when we used it requiring a filter order of only 72. The factor that needed to be included for for this function was r which was equivalent to the attenuation desired for the filter. This function guarantees that the attenuation will not be more than -r in decibels. The value are can be decreased and still provide the 80 dB attenuation desired; we were able to allow this value to drop as low as 68.