ECE 477 – Hardware Applications in C

Digital Multimeter

April 15, 2010

C. McGary, J. Castro

LCD Usage
 When initially deciding to use the LCD, we knew we would have problems with it. The LCD's are known to be difficult in setting it up to do what you want and there was no sample code for us to look at or use as a reference. To get the LCD to work, we would have to make the setup code and the code for printing to the screen ourselves. This was the hardest part of the code in terms of thinking required. We would have to know what all the pins are and what port we would use on the AVR. Then we would also need to know the proper instructions for setting up the LCD.

LCD Wiring
Initially, we realized that the LCD had 16 pin inputs but the datasheets we found said that there were only 14 pins used. I looked at the bottom of the LCD and found there to 14 lines coming from the input headers. This lead me to calling these pins the 14 we would use; these pin numbers were 1 – 13 and 15. The first three pins are strictly analog circuitry. Pin #1 is just the ground and Pin #2 was the the power supply (5V). The third pin is just for the contrast of the LCD where higher voltage would lighten the screen and ground would make it display at its greatest contrast. The next three pins were for setting up the commands for the LCD. These pins were set to use the 3 most significant bits (MSB) of PORT B, with the other half used by the circuitry for the mutimeter. The last 8 bits were connected to PORT D which we hadn't used yet. These bits will also be for transmitting commands, primarily characters.
Wiring notes provided by the datasheet can be seen below.

LCD Initialization
For initializing the LCD, we found a generic Hitachi HD44780 type initialization instruction set. The basic idea is this:
- Setup the display type
  - Choose the desired display type
  - Number of bits that will be sent at once
- Clear the Display
- Choose enter mode
  - Print left to right of right to left
  - shift the display?
- Choose display
  - Want the display on?
  - Want a cursor?
  - What the characters to blink?

For our setup, we decided to go with a 16:1 display type sending 8 bits at once. The display would print left to right without shifting the display; it would also show a cursor with no blinking. We decided on the 16:1 mux because that is the only setup our LCD would properly display, and we chose the 8 bits setup because this would make sending characters really simply.